## Slide 1
[P970] Introduction of download tool
Dec.22th, 2010 by Woon Rae Cho

## Slide 2
contents
Download procedure
Installation of download usb driver
3. USB driver recognition
4. Download Start
5. Download End
Download rom copy binary
Troubleshooting
Tool tip

## Slide 3
Download Procedure
MP-EHM
EBI2 ADDR
MCP
EBI2 DATA
EBI1 DATA
EBI1 ADDR
OMAP
SDRAM
2Gbit
NAND
Flash
4Gbit
DATA
DATA
ADDR
ADDR
CP
reset
MUIC
UART1
USB
UART
I2C(AP)
UART1
PC
Down Load Procedure
1. AP Boot Loader communicate with PC Tool using USB
2. CP Reset
3. CP Boot Loader D/L as using AP-CP UART
4. CP Program Data D/L as using UART
5. AP Program Data D/L
1
Internal
RAM
Internal
RAM
2
5
3
UART0
UART0
USB
SPI
SPI
4
[abbreviation]
- CP : Call Processor
- AP : Application Processor
- D/L : Down Load
- I/F : Interface
MCP
NAND
Flash
1Gbit
SDRAM
512Mbit

## Slide 4
Step 1 Installation of download USB driver
Execute ‘LG USB Driver 4.9.7 WHQL Release for Windows 7 .exe’ (refer under picture)

## Slide 5
Step 2 USB driver recognition
1. Execute smartflash tool
2. Separate battery from phone
3. Connect USB cable to phone
after pressing volume down key.
※ You should press volume UP
Key until PC recognize the USB driver
4. In smartflash tool, Press upper right
Button

## Slide 6
5. Install USB driver to specific COM port.
Wait until detecting USB COM port
‘LGE Mobile USB Serial Port’
6. If PC detects USB Com port,
You shoud disconnect USB cable
from Phone
Step 2 USB driver recognition

## Slide 7
7. You should confirm whether COM port is detected.
If COM port is not detected, you reconnect USB cable
to phone with pressing volume UP key.
Step 3 Download Start

## Slide 8
Step 3 Download Start cont…
9. Drag & Drop or Press ‘Add’ button
for adding files

## Slide 9
Important
In OMAP, specific files (“*.cfg” )
Must be included in download lists.
However, If you only want to download CP binary,
You don’t need to download *.cfg”
Step 3 Download Start cont…
9. Drag & Drop or Press ‘Add’ button
for adding files

## Slide 10
[AP]
Erase entire AP
You can erase all memory area of AP
2. Erase user data
You can erase USER and MISC partition
Step 3 Download Start cont…

## Slide 11
10. Press ‘Start’ button for flashing.
Step 3 Download Start cont…

## Slide 12
Step 3 Download Start cont…
11. You can find file lists for downloading.

## Slide 13
Step 4 Download End
12. You can see picture like right after finishing
download.

## Slide 14
Step 5 Multi Download
multi download
1. Add Files (AP binary)

## Slide 15
[P970] Introduction of rom copy bianry
download

## Slide 16
Download rom copy binary (Single download)
1. Add bin files (CP binary, AP binary)
single download

## Slide 17
Download rom copy binary (multi download)
multi download
1. Add bin files (CP binary, AP binary)

## Slide 18
[P970] Trobleshooting

## Slide 19
TroubleShooting
1. After downloading binary, Phone can’t boot.
Action1
When you download binary,
Check ‘erase user data(AP)
※ If there are some garbage data in
User partition, phone can’t boot.
Action2
Check battery whether battery
Is discharged

## Slide 20
2. During downloading, Color of progress bar turn into red color
Action1
(1) Disconnect USB cable from phone
(2) Reconnect USB cable to phone
(3) Restart download process.
TroubleShooting

## Slide 21
TroubleShooting
4. If FlashTool is disappeared
Action1
Click ‘Remove All’ button
Action2
Erase “SmartFlash.ini”
file
Action3
Restart FlashTool

## Slide 22
Tool tip
1. You can select download items that you want to
download using check.

## Slide 23
2. You can delete specific download item using ‘del’ key (In window keyboard) after selecting specific item
Tool tip

## Slide 24
Tool tip
3. Flashtool provides history function
Restart FlashTool
※ Flashtool always conserve download lists

## Slide 25
Tool tip
5. If you want to hidden log message, You can select mouse right button.

## Slide 26
Tool tip
6. If you want to save log message, You can select mouse right button.

## Slide 27
Log.rtf is MS word format.
So you can see using MS word
Tool tip